## Slide 1: Quantum Computing and its security implications
Jim Keeler, Ph.D.
Innotech Oklahoma City 11/1/18

## Slide 2: Outline
Introduction: Different types of computing
The basics What is quantum computing anyway?
  qubits
  Quantum entanglement
  Quantum information exchange
  Difficulties with quantum computing
What exists now
  Quantum key exchange
  Secure Quantum network communications
  Quantum annealing
What to expect in the next several years
  First commercial quantum computers
  Expansion of quantum networks
  Expansion of quantum key exchanges
What it all means
  Re-think encryption
  Use quantum networks

## Slide 3: Abstract
Quantum and promises to change the computing landscape in the near future. For example, cracking encryption that would take millions of years on a current supercomputer could be done in seconds on a quantum computer. This is no longer science fiction. D-Wave has shipped several quantum computers and IBM announced that they will have a quantum computer within two years. Quantum network encryption and quantum key exchange is available today via various companies. This presentation will help people understand quantum computing, how it works, what is available now and what the future may bring.

## Slide 4: Four types of computers
Digital Computer (Von Neumann Architecture)
Works on binary units, the type of computer that we all use.
Analog computer
Works on analog signals using resistors, capacitors & inductors to solve differential equations.
Quantum Computer
Works on qubits, quantum-entangled bits of information.
Parallel Distributed Processor (Neural Network/Brain)
Memory, processing & connectivity are all massively distributed.

## Slide 5: Types of computers (continued)
Digital computers
Good at integer-based math, rule-based expert systems, digital image processing, logic.
Not good at things like: factoring large primes, travelling salesman problems, solving distributed differential equations, pattern recognition, unconstrained control problems, etc.
Analog computers
Good at simulating differential equations.
Not good at things like: exact answers, logic, pattern recognition, unconstrained control problems.
Quantum computers
Good at solving certain classes of problems like factoring large primes, random walks, unordered data retrieval, etc.
Not good at things like: exact answers, logic, pattern recognition, unconstrained control problems.
Parallel distributed processors
Good at: Pattern recognition, unconstrained control problems, imagination, innovation, etc.
Not good at things like: Math, logic, reasoning, etc.

## Slide 6: What Quantum Computing can do
Factor primes
Encryption algorithms like RSA, SSL, etc. are based on the fact that factoring large primes (say 2048 bit) would take millions of years on a super computer.
Quantum computers could do this in minutes. (Yikes!)
Secure communications
Quantum-based networking allows perfectly secure communications. Any eaves-dropping on the signal destroys the signal, hence quantum networks are perfectly secure and invulnerable to hijacking.
Solve a variety of problems that are hard for digital computers
Random walk problems & classes of NP problems may be tractable with quantum computers.
But, they are not a panacea
They will not replace digital computers for day-to-day tasks. We will still need digital computers.
Solve quantum-mechanics/material science problems
What better to solve quantum mechanics problems than a quantum computer?

## Slide 7: How quantum computing works
The mysterious, magical qubits

## Slide 8: Qubits rely on Quantum entanglement
=
First we need to talk about superposition of quantum states.
Let’s start with Schrödinger’s Wave Equation:
Schrödinger’s Cat

## Slide 9: Quantum superposition and project management

## Slide 10: Quantum entanglement
Einstein called this “Spooky action at a distance”
It is as if there is a spooky connection that instantaneously tells one entangled particle the state of the other entangled particle no matter how far apart they are.
Einstein–Podolsky–Rosen paradox or EPR paradox
Entangled particles seem to communicate state information instantaneously even if they are separated by a great distance.

## Slide 11: Quantum entanglement
But how do we know that there aren’t just some hidden variables or hidden dimensions?
Bell’s Theorem proved the superimposed view of quantum mechanics. The math is a little hard, but we can demonstrate the basic idea with some coins.

## Slide 12: Quantum entanglement
OK, but you still haven’t told me what a qubit is.
What the heck is it?
A qubit is a quantum-entangled bit of information. Just like a bit is a 1 or a 0, a qubit is two entangled states that either could be one or zero, but is both 1 and 0 at the same time.
Typically a qubit is an entangled pair of photons, electrons, or nuclei. The entangled part is the spin of the particle (spin up versus spin down). The spin can be measured with an electromagnetic field, and can be manipulated (flipped, if you will) with a pulse of radio-frequency energy, or measured via a light polarizer.

## Slide 13: 2 qubit example
α
β
γ
δ
Because the particles are in superimposed states, it takes four numbers to specify the state of these two entangled particles, whereas in a binary system it only takes two numbers (e.g. 0,1).
More generally, a quantum computer with N spins requires 2N numbers to describe the state of the system (compared to N numbers for a binary computer).
(0,0)
(1,0)
(0,1)
(1,1)
0.2
0.4
0.1
0.3

## Slide 14: Enormous quantum power
Example:
A 64-bit computer can perform manipulation on 64 -bit binary numbers at a time.
A 64-qubit quantum computer operates in a space of 264 dimensions, or roughly 16,000,000,000,000,000,000 (16*1018)numbers to specify the state of the quantum system.
Using cleverly crafted quantum algorithms and “quantum gates”, the computation can happen in this enormous space in parallel – it is as if all of the answers were being evaluated simultaneously, and the quantum system freezes out the right answer from this vast space.
It also means you double the power with every added qubit.
To double the power of a digital computer 32bits -> 64 bits
To double the power of a quantum computer 32qubits -> 33 qubits

## Slide 15: Standard computing versus Quantum
B
A
Sum
Carry
Half Adder Circuit
Binary values are represented by electric signals:
0 = no current, 1 = current

## Slide 16: Standard computing versus Quantum
B
A
Sum
Carry
0
0
0
0
EXOR
AND

## Slide 17: Standard computing versus Quantum
B
A
Sum
Carry
1
0
1
0
EXOR
AND

## Slide 18: Standard computing versus Quantum
B
A
Sum
Carry
1
1
0
1
EXOR
AND

## Slide 19: Standard computing versus Quantum
B
A
0
CIN
Full Adder Circuit
COUT
Quantum Circuit example
measure
Sum
1
Hadamard CNOT combo

## Slide 20: So what can Quantum computers do?
Example 1: Shor’s algorithm
An algorithm that runs on a quantum computer that finds the prime factors of a number N and does it in polynomial time (rather than exponential time as on a digital computer). What would take a normal supercomputer tens of millions of years can be done in minutes on a quantum computer.
  Note: Since most encryption algorithms such as PGP and RSA rely on a public key N which is composed of two large primes, quantum computers could crack that encryption in minutes rather than millions of years on a digital computer.
Example 2: Grover’s algorithm
Grover's algorithm searches an unstructured database (or an unordered list) with N entries, for a marked entry, using only O() queries instead of the Ω(N) queries required classically.

## Slide 21: Quantum communication
Unhackable Communication
Using the properties of quantum entanglement, quantum communication is immune to “man-in-the-middle” eavesdropping.
Anyone trying to listen to the communication breaks the entanglement, rendering the eavesdropping useless.

## Slide 22: Quantum communication (BB84 algorithm)
Alice
Laser
Optical channel
Polarizer
Detector
Bob
Polarizer
Eve (Eavesdropper)

## Slide 23: Is this just Science Fiction?
Several companies are offering commercial quantum key distribution systems: ID Quantique (Geneva), MagiQ Technologies, Inc.(New York), QuintessenceLabs (Australia) and SeQureNet (Paris).
Several other companies also have active research programs, including Toshiba, HP, IBM, Mitsubishi, NEC and NTT
In 2004, the world's first bank transfer using quantum key distribution was carried out in Vienna Austria using ID Quantique systems.
Commercial QKD is more than a decade old

## Slide 24: Is this just science fiction?
D-wave already has quantum annealing computers
2000 qubit available now and 4000 bit available soon: http://www.nature.com/news/d-wave-upgrade-how-scientists-are-using-the-world-s-most-controversial-quantum-computer-1.21353
IBM, Google, Microsoft, Intel and others are all in a race for the quantum computer
Intel announced 49-qbit chip in January 2018
  https://spectrum.ieee.org/tech-talk/computing/hardware/intels-49qubit-chip-aims-for-quantum-supremacy
Google a 72-qbit quantum computer in March 2018
https://www.sciencenews.org/article/google-moves-toward-quantum-supremacy-72-qubit-computer
China and others are working on satellite-based Quantum Key Distribution. Demonstrated > 1,000KM this year.
http://www.nature.com/news/chinese-satellite-is-one-giant-step-for-the-quantum-internet-1.20329

## Slide 25: D-wave quantum computer

## Slide 26: IBM Atlas quantum computer

## Slide 27: IBM Free Quantum computer in the cloud https://quantumexperience.ng.bluemix.net/qx/experience

## Slide 28: 3 types of quantum computers
Not all quantum computers are equal
Quantum Annealing computer
Analog Quantum Computer
Universal Quantum Computer

## Slide 29: 1: Quantum Annealing
From: http://www.visualcapitalist.com/three-types-quantum-computers/
Bottom Line: A very specialized form of quantum computing with unproven advantages over conventional computing. D-Wave is one example. Google claimed a particular problem was solved 3000 times faster than conventional computers in a demo.
Generality of Applications
Restricted
Partial
Universal
Computational Power
Low
Med
High
Difficulty
Level
Easy
Med
Hard
Optimization Problems
Quantum Annealer
The quantum annealer is the least powerful and most restrictive form of quantum computers. It is the easiest to build, yet can only perform one specific function. The consensus is that a quantum annealer has no known advantages over conventional computing.
Similar to traditional computers
Easiest to build

## Slide 30: 2: Analog Quantum
From: http://www.visualcapitalist.com/three-types-quantum-computers/
Bottom Line: The most likely form of quantum computing that will first show a true quantum speedup over conventional computing. This could happen within the next five years.
Generality of Applications
Restricted
Partial
Universal
Computational Power
Low
Med
High
Difficulty
Level
Easy
Med
Hard
Quantum chemistry
Material science
Optimization Problems
Sampling
Quantum Dynamics
Analog Quantum
The analog quantum computer will be able to simulate complex quantum interactions that are intractable for any known conventional computer. It is conjectured that the analog quantum computer will contain between 50 and 100 qubits.
Millions of times faster than conventional computers on special problems
Moderately hard to build

## Slide 31: 3: Universal Quantum
From: http://www.visualcapitalist.com/three-types-quantum-computers/
Bottom Line: This is the “holy grail” of quantum computing, offering the potential to be exponentially faster than traditional computers for a number of important problems.
Generality of Applications
Restricted
Partial
Universal
Computational Power
Low
Med
High
Difficulty
Level
Easy
Med
Hard
Secure computing
Machine Learning
Cryptography
Searching
+ all of Analog Quantum.
Universal Quantum
The universal quantum computer is the most powerful, the most general, and the hardest to build. It poses a tremendous number of technical challenges. Only about 8,000 is estimated to crack RSA-2048).
Many trillions of times faster than conventional computers
Extremely hard to build

## Slide 32
Gartner Hype Cycle.
Gartner projects a $5B market by 2020 worth perhaps >$100B in ten years

## Slide 33: Scaling in quantum computing
Qubits in computers announced over the past 5 years
Danger zone:
2048 bit encryption
Can be cracked

## Slide 34: Post-Quantum world
There is a good chance that quantum computers will be able to crack RSA-2048 within five-ten years (need about 8,000 qubits in a universal computer to do this).
Some encrypted data has a shelf-life of more than ten years. It may take ten years to cut over to a new encryption scheme, so companies and governments are scrambling to figure out what to do.
Most encryption used today is not safe in a quantum world.
If someone has been recording a https session, say, they may not be able to decrypt it now, but a few years from now, who knows.
There are encryption algorithms that are safe:
Secure communications will move to symmetric encryption or hash algorithms, or perhaps lattice algorithms.
QKD will likely be more popular for the most sensitive communications
Some governments and banks are already starting to use “Quantum Safe” algorithms, and this is expected to increase over the next decade.

## Slide 35: Post-Quantum Algorithm Assessment
Grover’s Algorithm cuts these in 1/2
Shor’s Algorithm blasts these apart

## Slide 36: Start thinking post-quantum now
It may take 5-10 years to replace infrastructure & software
It is good advice, I think, to start moving to a post-quantum secure world now.
Here is a good place to start
https://csrc.nist.gov/Projects/Post-Quantum-Cryptography

## Slide 37: Questions?
Some of the best videos explaining quantum computers:
https://www.youtube.com/watch?v=JRIPV0dPAd4
https://www.youtube.com/watch?v=zNzzGgr2mhk
Some other links:
https://www.technologyreview.com/s/603495/10-breakthrough-technologies-2017-practical-quantum-computers/
https://www.technologyreview.com/s/604242/googles-new-chip-is-a-stepping-stone-to-quantum-computing-supremacy/
E-mail me if you have any questions/comments: dr.jkeeler@gmail.com